## Slide 1
The University of Pittsburgh School of Computing and Information, CS PhD Program
Connor Sweeney and Donte DiFrancesco
EMS Priority Traffic Control Capstone
INTRODUCTION
OBJECTIVES
RESULTS & CONCLUSIONS
EMS (Emergency Medical Service) vehicle travel time should be the top priority on the road.
Adaptable traffic signals (signals that change according to EMS presence) are used to attempt to reduce EMS travel time.
Our objectives were to develop and test different EMS priority policies. These policies dictated what would happen to the adaptive traffic signals when an EMS vehicle approached them.
We initially planned on using CityFlow because of its efficient performance with reinforcement learning, however we discovered that it did not have the functionality our research required.
We began using another program, SUMo (Simulation of Urban Mobility), because it had fully implemented EMS vehicle functionality.
METHODS
Simulation Programs
Chart: EMS Travel Time by Priority
| 1 | 2 | 3 | 4 | 5 | 7 | 8 | 11 | 12 | 13 | 14 | 15 | 18 | 19
Green Corridor | 51 | 76 | 51 | 69 | 56 | 62 | 70 | 67 | 69 | 71 | 49 | 51 | 60 | 50
Red Freeze | 54 | 73 | 62 | 69 | 63 | 62 | 67 | 57 | 64 | 62 | 54 | 58 | 57 | 45
Control | 84 | 109 | 72 | 130 | 174 | 94 | 83 | 80 | 70 | 77 | 95 | 88 | 74 | 60
Chart: Congestion Clearing Time vs. Traffic Density
| 1 | 2 | 3 | 4 | 5 | 7 | 8 | 11 | 12 | 13 | 14 | 15 | 18 | 19
Green Corridor | 3980 | 2030 | 1364 | 1060 | 833 | 626 | 551 | 395 | 386 | 374 | 374 | 339 | 294 | 281
Red Freeze | 4072 | 2117 | 1371 | 1105 | 929 | 647 | 587 | 445 | 402 | 401 | 385 | 348 | 294 | 295
Control | 4096 | 2056 | 1378 | 1031 | 865 | 657 | 604 | 507 | 406 | 380 | 385 | 318 | 292 | 301
■ Green Corridor
■ Red Freeze
■ Control
Green Corridor
  This policy turns all lights for EMS lanes green until the EMS passes
Red Freeze
  This policy makes every light red until EMS cuts through the intersection
EMS Travel Time
  Measured in simulation steps it takes EMS to get from point A to point B
Impact on Congestion
  Measured in simulation steps it takes resulting congestion to clear
EMS Policies
Data Metrics to Analyze
This image shows a SUMo simulation of an intersection with an EMS vehicle splitting a lane.
Our first experiment, EMS Travel Time by Priority shows that both Green Corridor and Red Freeze traffic policy implementations decrease the travel time of EMS regardless of traffic congestion.
Our second experiment, Congestion Clearing Time vs. Traffic Density, shows that the policies – which temporarily change the pattern of traffic signals – do not increase congestion after their use.
These results are exciting because they show that not only was our implementation of EMS priority policies able to get EMS vehicles to their destinations faster, but it did not increase resulting congestion. This means that in our simulations, the implementation of EMS priority policies has a net benefit to the performance of traffic systems.