## Slide 1
Our first metric, EMS Travel Time, shows that both the Green Corridor and Red Freeze traffic policies decrease the travel time of EMS vehicle, with Green Corridor reducing it by 47.25%.
University of Pittsburgh – School of Computing and Information – CS Capstone Project
Connor Sweeney and Donte DiFrancesco
EMS Priority Traffic Control Capstone
INTRODUCTION
Objectives
RESULTS & CONCLUSIONS
EMS (Emergency Medical Service) vehicle travel time should be the top priority on the road.
Adaptable traffic signals (signals that change according to EMS presence) are used to attempt to reduce EMS travel time.
We initially planned on using CityFlow because of its efficient performance with reinforcement learning, however we discovered that it did not have the functionality our research required.
TOOLS
Initial Hurdle
■ Green Corridor
■ Red Freeze
■ Control
Green Corridor
  This policy activates green lights for the next three signals in the EMS vehicle’s route.
Red Freeze
  This policy makes all lights in the next intersection red while the EMS vehicle is passing through it.
EMS Travel Time
  Measured in seconds it takes the EMS vehicle to get from point A to point B
Congestion Clearing Time
  Measured in seconds it takes resulting congestion to clear
Traffic Signal Policies
Data Metrics to Analyze
Simulation intersection with an EMS vehicle lane splitting
These results are exciting because they suggest that not only was our implementation of EMS priority policies able to get EMS vehicles to their destinations faster but, in most cases, it did not increase resulting congestion. This means that in our simulations, the implementation of EMS priority policies has a net benefit to the performance of traffic systems.
Develop scenarios that mimic real-world traffic
Gather data about how adaptive traffic signals affect the network
Analyze the data
We transitioned to another program, SUMO, because it had fully implemented EMS vehicle functionality.
Simulation of Urban Mobility
Collaboration
Discord
Trello
GitHub
Analysis
SUMO – Create simulations
Traci – Modify traffic signal behavior and collect data
Excel – Visualize data
Chart: EMS Travel Time vs Traffic Density (Average over ten simulations)
| Light | Medium | Heavy
Green Corridor | 30 | 43 | 48
Red Freeze | 41 | 62 | 66
Control | 46 | 79 | 91
Chart: Congestion Clearing Time vs Traffic Density (Average over ten simulations)
| Light | Medium | Heavy
Green Corridor | 183 | 339 | 636
Red Freeze | 221 | 364 | 699
Control | 203 | 375 | 706
Our second metric, Congestion Clearing Time, shows that the traffic policies – which temporarily change the pattern of traffic signals – do not significantly increase congestion after their use. In fact, the green corridor reduces it by 9.92%.